## Slide 1: Types of transformers

## Slide 2: Transformer Construction
The transformer has two coils and the mutual inductance laminated steel core. The two coils are insulated from each other and from the steel core. The core is made out of transformer sheet steel laminations assembled to provide a continuous magnetic path with minimum of air-gap included.

## Slide 3: Core- Type Transformer
In core-type transformer, the windings are given to a considerable part of the core. The coils used for this transformer are form-wound and are of cylindrical type. Such a type of transformer can be applicable for small sized and large sized transformers.

## Slide 4: Shell-Type Transformer
In shell-type transformers the core surrounds a considerable portion of the windings. Paper is used to insulate the different layers of the multi-layer discs. The whole winding consists of discs stacked with insulation spaces between the coils. These insulation spaces form the horizontal cooling and insulating ducts.

## Slide 5
Such a transformer may have the shape of a simple rectangle or may also have a distributed form.

## Slide 6: Types of cooling
Oil Filled Self-Cooled Type
Oil Filled Water Cooled Type
Air Blast Type

## Slide 7: Oil Filled
The tank is filled with purified, high quality insulating oil. The oil helps in transferring the heat from the core and the windings to the case from where it is radiated out to the surroundings.

## Slide 8: Air Blast
A transformer is cooled by forcing a circulation of air around its windings.

## Slide 9: Some types of transformers
Distribution Transformer
Polyphase transformers
Power Transformer
Control Transformer
Auto Transformer
Isolation Transformer
Instrument Transformer
Audio Transformer
Leakage Transformer

## Slide 10
Distribution transformers are generally used in electrical power distribution and transmissionsystems. This class of transformer has the highest power.
Polyphase transformers With three or more input and output windings.
Power Transformer are sometimes considered to be those with ratings of 300 volt-amperes and below.
Control Transformer are generally used in electronic circuits that require constant voltage orconstant current with a low power or volt-amp rating.

## Slide 11: Auto Transformer
The auto transformer is generally used in low power applications where a variable voltage is required.

## Slide 12: Instrument Transformers
Potential Transformer steps down voltage of a circuit to a low value that canbe effectively and safely used for operation of instruments such as ammeters, voltmeters, wattmeters, and relays used for various protective purposes
Сurrent transformer steps down the current of a circuit to a lower value andis used in the same types of equipment as a potential transformer.